بسمه تعالي

آگهي فراخوان عمومي شناسايي توليدكنندگان داخلي مواد شيميائي

شركت مجتمع گاز پارس جنوبي در نظر دارد نسبت به شناسايي توليد كنندگان واجد صلاحيت مواد شيميائي تحت شرايط ذيل اقدام نمايد :

| شرايط شركت در مناقصه | مدارك مورد نياز |
| --- | --- |
| داشتن شخصيت حقوقي/ يا حقيقي | 1.ارسال نامه اعلام آمادگي و درج شناسه ملي جهت شركت در مناقصه 2.ارائه تاييديه از اداره ثبت شركتها مبني بر آخرين تغييرات و اساسنامه شركت بهمراه نشاني دقيق شركت/كارخانه براي اشخاص حقوقي 3.ارائه جواز كسب از صنف مربوط به اقلام مورد نياز مجتمع گاز پارس جنوبي براي اشخاص حقيقي |
| داشتن توانايي مالي براي تامين اقلام و ارائه ضمانت بانكي و يا واريز وجه نقد جهت شركت در فرآيند ارجاع كار به مبلغ 000/000/000/0 ريال | ارائه يكي از مدارك ذيل جهت ارزيابي توانايي مالي مطابق جدول شماره 1 1.ارائه اظهارنامه مالياتي و ارائه اسناد مالياتهاي قطعي و علي الحساب پرداخت شده در پنج سال گذشته 2.فروش آخرين سال توليد مستند به قراردادها و اسناد فروش يا صورتهاي مالي تأييد شده در پنج سال گذشته 3.دارايي‌هاي ثابت مستند به اظهارنامه رسمي يا گواهي بيمه دارايي‌ها |
| حسن شهرت | 1.تكميل جدول خود اظهاري شماره 2-2 2.ارائه تاييديه يا رضايتنامه از مشتريا ن قبلي |
| استاندارد بودن محصولات | 1.ارائه گواهينامه هاي مربوطه جهت ارزيابي مطابق جدول شماره 3 |
| داشتن تجربه و دانش لازم | 1.ارائه مدارك مثبته در خصوص ساخت و يا تامين كالاهاي مشابه با موضوع مناقصه با توجه به جدول شماره 4 |
| حسن سابقه شركت | 1.جدول شماره 2 ملاك ارزيابي جدول شماره5 مي باشد . 2. ارائه تاييديه از مشتريا ن قبلي در مورد انجام كارهاي مشابه با ذكر نام خريدار ، حجم يا ارزش تقريبي معامله انجام شده و اطلاعاتي كه توانمندي پيشنهاد دهنده را براي عرضه كالاي مورد نظر به اثبات برساند . |
| با كيفيت بودن مواد اوليه مصرفي | 1.ارائه گواهي كيفيت مواد اوليه توليد مطابق جدول شماره 6-1 و اعلام نحوة تضمين و گارانتي محصولات مطابق جدول 6-2 |
| داشتن توانايي ارائه پيشنهادات فني و مالي در مدت زمان حداكثر 14 روز | حداقل امتياز قابل قبول در ارزيابي كيفي 50 مي باشد هنگام عقد قرار داد با برنده، ارائه صورت هاي مالي حسابرسي شده از سوي شركت برنده الزامي مي باشد . |
| مبلغ برآوردي | 000/000/000/000 ريال |

از متقاضياني كه توانايي احراز شرايط عمومي را داشته و قادر به ارائه مدارك مورد نياز ميباشند ، دعوت مي‌گردد حداكثر 14 روز پس از درج آگهي نوبت دوم مدارك  ، سوابق كاري و همچنين نامه اعلام آمادگي خود را به آدرس استان بوشهر ـ بندر عسلويه ـ منطقه ويژه اقتصادي انرژي پارس ـ شركت مجتمع گاز پارس جنوبي ـ پالايشگاه فاز 2و3 ـ مديريت بازرگاني  ـ اداره  خريد ـ صندوق پستي 311-75391  تلفن: 07731312242-07731312248  ، نمابر: 6-07737325435 جهت ارزيابي و تعيين صلاحيت ارسال نمايند (ارزيابي صلاحيت متقاضيان مطابق جدول شماره 7 صورت مي پذيرد)  .

واحد مديريت بازرگاني اين مجتمع پس از بررسي و كنترل مدارك ارسالي ، نتيجه ارزيابي خود  را  بر اساس فرم ارزيابي اوليه تامين كنندگان كالا و شاخص هاي ارزيابي به اطلاع داوطلبان واجد صلاحيت خواهد رساند .

بديهي است شركت مجتمع گاز پارس جنوبي در كليه مراحل ( بررسي مدارك ، تعيين صلاحيت ، بررسي اسناد مالي و فني و ... )  و تحت هر شرايط مختار ميباشد .

شرح اقلام مورد نياز

| Item | Description |
| --- | --- |
| 1 | ANTI-FOAM (DEFOAMER), "BELITE M8" ANTI-FOAM, "BELITE M8" APPEARANCE: LIQUID COLOR: LIGHT YELLOW BOILING POINT(INTERVAL): 80 DEG.C. (ISOPROPANOL) DENSITY(SPECIFIC GRAVITY): 0.95-1 G/ML PH VALUE, DILUTED SOLUTION: 6.5-7.5 VISCOSITY(INTERVAL): 200 CST. AT 20 DEG.C. SOLUBILITY: SLIGHTLY SOLUBLE IN WATER FLASH POINT: 30 DEG.C. AUTO IGNITION TEMP. : APPROX. 450 DEG.C. PARTITION COEFFICIENT: MUCH LESS THAN 3 SUPPLIER: "ARABAUST WATERTEK" OR "BIOLAB" LOCATION: SOUTH PARS ANTI-FOAM BELITE M8 |
| 2 | ANTI-FOAM, SAG-7133, ORGANOSILICON EMULSION ANTI-FOAM (DEFOAMER), ORGANOSILICON EMULSION FOR D.E.A (DIETHANOLAMINE) GAS TREATING SYSTEM COLOUR: OPAQUE WHITE, ODOR: MILD MELTING POINT: 0 DEG.C. (APPROXIMATELY) RELATIVE DENSITY: 1.004 AT 25 DEG.C.(1.013 HPA) BOILING POINT: MORE THAN 100 DEG.C. AT 1.013 HPA VAPOUR PRESSURE: LESS THAN 35.91 HPA AT 20 DEG.C. VAPOUR DENSITY(AIR=1): HEAVIER THAN AIR SOLUBILITY IN WATER: DISPERSIBLE REF:WITCO(EUROPE)SA SAG-7133,OR CROMPTON SA. OSI SPECIALTIES OR APPROVED EQUIVALENT LOCATION:SHAHID HASHEMI NEGAD, SOUTH PARS, PHASES 2 & 3, 12 AND ILAM GAS REFINERY NOTE:ANTI-FOAM SHALL BE PACKED IN AIR TIGHT NEW HEAVY GAUGE STEEL OR PLASTIC DRUMS NOTE:DRUMS SHALL BE MARKED WITH: CHEMICAL NAME, DATE OF MANUF. ORDER NO., MESC NO., ANTI-FOAM,ORGANOSILICON EMULSION |
| 3 | ANTI-FOAM, BASED ON ETHYLENE DIAMINE ANTI-FOAM (DE-FOAMER) EMULSIFIER, LOW FOAMING DISPERSANT AGENT LIQUID CHEMICAL BASED ON ETHYLENE DIAMINE APPEARANCE: CLEAR, LIGHT YELLOW LIQUID DENSITY AT 20 DEG.C. : 1.03 -/+ 0.5 G/CM3 PH (1% SOLUTION): 10.5 -/+ 0.5 SENSITIVITY TO FREEZING: BELOW 0 DEG.C. REF: SIMILAR TO TYPE PN 30 PN 30 OR OMC 532 E |
| 4 | PHTHALOCYANINE CATALYST, "EUROPHTAL-8020" PHYSICAL STATE: LIQUID COLOR: BLUE PH : 7-9 DECOMPOSITION TEMPERATURE: MORE THAN 300 DEG.C. RELATIVE DENSITY(WATER): 1.15 SOLUBILITY: SOLUBLE IN WATER REF: FRENCH PETROLEUM INSTITUTE |
| 5 | METHYL DEA METHYL DIETHANOL AMINE (MDEA) SOLVENT SUITABLE FOR GAS SWEETENING PLANT MIN. CONCENTRATION: 99.6% COLOUR: COLOURLESS-YELLOW, ODOUR: AMINE-LIKE OCTANOL/WATER PARTITION COEFFICIENT: -1.08 MELTING POINT: -21 DEG.C. BOILING POINT: 243 DEG.C. FLASH POINT:(DIN 51758)137 DEG.C.,(DIN 51755) 126 DEG.C. EXPLOSION LIMITS: LOWER 0.9/UPPER 8.4 VOL.% VAPOUR PRESSURE (40 DEG.C.) 0.026 MBAR IGNITION TEMP. 265 , VISCOSITY(20C) 101 MPO DENSITY (20 DEG.C.) 1.04 G/CM3 SOLUBILITY IN WATER (20 DEG.C.) FULLY MISCIBLE PH VALUE (AT 100 GIL, 20 DEG.C.) 11.5 SECONDARY AMINES: <= 0.05% WATER: (19E322) <=0.1% REF: BASF OR APPROVED EQUIVALENT |
| 6 | : FILTER AID : CHEMICAL, FILTER AID DIATROSE 0 : COMPONENTS:BLEACHED CELLULOSE 100% : SOLUBILITY:SOLUBLE IN CUPRIETHYLENEDIAMINE(C2H6CUN2) : FIBRE CHARACTERISTICS: AVERAGE LENGTH:1.3 MM : AVERAGE DIAMETER:15 MICRON : COMPOSITION SUBSTA.:CELLULOSE,CELLOULOSE POLYMER(C6H10O5)N : PHYSICAL CHARACTERISTICS:PULEVERLENT PRODUCT : COLOUR:WHITE,PH:6.25+1.25 : SELF INFLAMATION TEMPERATURE:>200 DEG.C : SUPPLIER:EUROFILTEC |
| 7 | : REFRIGERANT GAS, R134A : REFRIGERANT, TETRAFLUOROETHANE : MOLECULAR FORMULA: C2H2F4 : DENSITY: 4.25 KG/M3 : MELTING POINT: -103.3 DEG.C. : BOILING POINT: -26.3 DEG.C. : MANUFACTURER: "FROGEN" UK. : "DUPONT" OR "HONEYWELL" : REFRIGERANT R134A : IN 50 TO 250 KG CYLINDER |
| 8 | : REFRIGERANT GAS, R134A : REFRIGERANT, TETRAFLUOROETHANE : MOLECULAR FORMULA: C2H2F4 : DENSITY: 4.25 KG/M3 : MELTING POINT: -103.3 DEG.C. : BOILING POINT: -26.3 DEG.C. : MANUFACTURER: "FROGEN" UK. : LOCATION: SOUTH PARS, PHASES 17,18, 4,5 : "DUPONT" OR "HONEYWELL" : IN APPROVED CYLINDER 13.5 KG |
| 9 | REFRIGERATION GAS, 407C : FORM: LIQUIFIED GAS : COLORLESS : ODOR: SLIGHT, PH: NEUTRAL : BOILING POINT/RANGE: -43.9 DEG.C. (-47 DEG.F.) : VAPOUR PRESSURE: 10.769 HPA AT 21.1 DEG.C. : VAPOUR PRESSURE: 24.593 HPA AT 54.4 DEG.C. : RELATIVE VAPOUR DENSITY: 3 : DENSITY: 1.16 G/CM3 AT 21.1 DEG.C. (70 DEG.F.) : WATER SOLUBILITY: 1.5 G/LT. : MANUFACTURER: GENETRON 407C "HONEYWELL" OR "DUPONT" : NOTE: USED FOR ELECTRICAL WATER CHILLER : "CARRIER" FRANCE, TAG: 176-K-X01A/B : IN APPROVED CYLINDER 13.5 KG |
| 10 | : REFRIGERANT GAS, CHLORODIFLUOROMETHANE, CHCLF2, R22 : FORM: LIQUIFIED GAS : COLORLESS : ODOR: SLIGHT, MOLECULAR WEIGHT: 86.46 G/MOL : PH: NEUTRAL : MELTING POINT/RANGE: -160 DEG.C. (-256 DEG.F.) : BOILING POINT/RANGE: -40.8 DEG.C. (-41.4 DEG.F.) : VAPOUR PRESSURE: 136.1 PSIA : VAPOUR PRESSURE: 21.470 HPA AT 54.4 DEG.C.(129.9 DEG.F.) : RELATIVE VAPOUR DENSITY: 3 : WATER SOLUBILITY: 3 G/LT. : MANUFACTURER: "FROGEN" UK. : NOTE: USED FOR SPLIT UNIT/WINDOW TYPE COOLER : "CARRIER" FRANCE OR "LG" : GENETRON R22 "HONEYWELL" OR "DUPONT" : 13.5 KG CYLINDER |
| 11 | : REFRIGERANT GAS, C2HCL2F : SUPPLIER: "ISCEON" R141B OR EQUIVALENT. : NOTE: FOR USE IN ALL HVAC UNITS : REFRIGERANT GAS : IN CONTAINER ABOVE 200 KG |
| 12 | : CORROSION INHIBITOR, ANTI ACID CORROSION, NORUST GL 50 : CORROSION INHIBITOR, NEUTRALIZE SYSTEM ACIDITY : APPEARANCE AT 25 DEG.C.: LIQUID : DENSITY AT 25 DEGC.C.: 1280 KG/M3 : TOTAL ALKALINITY: 2.40 ML HCL N/G : VISCOSITY AT 20 DEG.C.: 25 MPA(CP) : VISCOSITY AT 0 DEG.C.: 100 MPA(CP) : PH:AROUND 12, FREEZING POINT:AROUND -15 DEG.C. : SOLUBLE IN WATER, ALCOHOLS, AND GLYCOLS. : INSOLUBLE IN HYDROCARBONS : SUPPLIER: "CECA" NORUST GL50, FRANCE |
| 13 | CATION EXCHANGE RESIN, AMBERJET 1500H : PHYSICAL FORM: DARK AMBER SPHERICAL BEADS : MATRIX: STYRENE DIVINYLBENZENE COPOLYMER : FUNCTIONAL GROUP: SULFONATE : IONIC FORM AS SHIPPED: H+ : TOTAL EXCHANGE CAPACITY: > 2.00 EQ/L : MOISTURE HOLDING CAPACITY: 45 TO 51% : SPECIFIC GRAVITY: 1.28 TO 1.32 (NA+ FORM) : PARTICLE SIZE (UNIFORMITY COEFFICIENT) <1.20 : PARTICLE SIZE (HARMONIC MEAN SIZE): 650-/+50 MICRON : PARTICLE SIZE (FINES CONTENT) <0.425 MM.: 0.5% MAX. : MAXIMUM REVERSIBLE SWELLING: NA+ H+ : 8% : REF: SIMILAR TO TYPE "AMBERJET 1500H" "ROHM & HAAS" : CATION EXCHANGE RESIN |
| 14 | ANION EXCHANGE RESIN : PHYSICAL FORM: LIGHT AMBER SPHERICAL BEADS : MATRIX: STYRENE DIVINYLBENZENE COPOLYMER : FUNCTIONAL GROUP: TRIMETHYL AMMONIUM : IONIC FORM AS SHIPPED: CL- : TOTAL EXCHANGE CAPACITY >1.40 EQ/L (CL- FORM) : MOISTURE HOLDING CAPACITY: 40 TO 48% (CL- FORM) : PARTICLE SIZE(UNIFORMITY COEFFICIENT) <1.20 : PARTICLE SIZE(HARMONIC MEAN SIZE) 0.53 TO 0.63 MM. : PARTICLE SIZE( <0.425 MM.) 0.5% MAX. : MAXIMUM REVERSIBLE SWELLING: CL- OH- <30% : REF: SIMILAR TO TYPE "AMBERJET 4400 CL" "ROHM & HAAS" |
| 15 | : ANIONIC RESIN, STRONGLY BASIC, MACROPOROUS : FOR DECOLORIZATION OF FOOD STREAMS, REVERSIBLE : ORGANIC SUBSTANCES ADSORPTION. : MATRIX: STYRENE DIVINYLBENZENE COPOLYMER : MOISTURE CONTENT: 56-64% : EXCHANGE CAPACITY: MORE THAN 0.80 EQ/L : APPEARANCE: BEADS, SPECIFIC GRAVITY: APPROX. 1.06 : ODOR: SLIGHT SMELL OF AMINE : OPERATING PH RANGE: 0-14 : REVERSIBLE SWELLING: CL-,OH-: 25% MAX. : OPERATING TEMPERATURE: 85 DEG.C. : REF: "APPLEXION" TYPE XA 4041 CL OR APPROVED EQUIVALENT. : PARTICLE SIZE: 0.4-1.25 MM. : FINEST CONTENT:<0.3MM.(50MESH) |
| 16 | CATIONIC RESIN, WITH HIGH CAPACITY AND EXCELLENT : MECHANICAL, OSMOTIC STABILITY FOR SOFTENING OF SUGAR : SOLUTIONS AND ORGANIC PRODUCTS. : MATRIX: CROSS-LINKED POLYACRYLATE : EXCHANGE CAPACITY: MORE THAN 3.9 EQ/L : MOISTURE CONTENT: 54-58% : MODIFIED ACRYLIC COPOLYMER : PHYSICAL STATE: BEAD,UNIFORMITY COEFFICIENT:LESS THAN 1.8 : COLOR: PALE YELLOW, SPECIFIC GRAVITY: APPROX. 1.16 : OPERATING PH RANGE: 5-14 : REVERSIBLE SWELLING: H+,NA+: 60% MAX. : OPERATING TEMPERATURE: 80 DEG.C. MAX. : REF: "APPLEXION" TYPE XA 1041 FG OR APPROVED EQUIVALENT. : PARTICLE SIZE:0.3-1.2 MM. |
| 17 | COAGULANT, "RBW80108" FLOATATION REAGENT : IT IS A LIQUID CATIONIC POLYAMINE PRIMARY COAGULANT : RECOMMENDED FOR USE IN TREATMENT OF INDUSTRIAL WATERS : TO REMOVE SUSPENDED SOLIDS IN SEDIMENTATION APPLICATIONS. : APPEARANCE: LIQUID : COLOR: RED BROWN : ODOR: CHARACTERISTIC : MELT/FREEZE POINT: LESS THAN -3 DEG.C. : DENSITY/SPECIFIC GRAVITY: 1.11-1.18 G/ML : VISCOSITY: APPROX. 180 CST. : SOLUBILITY : SOLUBLE IN WATER : SUPPLIER: BAKER HUGHES |
| 18 | QUINOLINE (SULFUR DEGASING AGENT) : APPEARANCE: LIGHT YELLOW LIQUID : ODOR: PECULIAR ODOR : SOLUBILITY : SOLUBLE IN WATER : SPECIFIC GRAVITY AT 25 DEG.C. : 1.091 : PH: WEAK BASE : BOILING POINT: 237 DEG.C. : MELTING POINT: -15 DEG.C. : VAPOUR PRESSURE: 1 MMHG AT 59.7 DEG.C. |
| 19 | CORROSION INHIBITOR, ARMOHIB 31 : FORM: LIQUID, SPECIFIC GRAVITY AT 25 DEG.C.: 1.042 : POUR POINT: 24 DEG.F., FLASH POINT: 340 DEG.F. : CLOUD POINT: 28 DEG.F., SOLUBLE IN ACID : APPLICATION: ALIPHATIC NITROGEN INHIBITORS RETARD THE : CORROSIVE EFFECT OF ACIDS ON METALS DURING PICKLING, : PROCESS EQUIPMENT CLEANING, AND OIL WELL ACIDIZING OPERATION : SUPPLIER: ARMOHIB 31 "ROSOUBGIRI CO." |
| 20 | : ACTIVATED CARBON, "NORIT" ROY : MEDIA TYPE: NORIT EXTRUDED GRADES : IODINE NO. 950 MIN., BALL-PAN HARDNESS 95 MIN. : PARTICLE SIZE:<0.60 MM. MAX. 0.5 MASS% : MOISTURE(AS PACKED): 5 MASS% MAX. : SI ELUTION AFTER 10 BV: 0.1 MG/L : REF: "NORIT" ROY 0.8 OR EQUIVALENT. |
| 21 | ACTIVATED CARBON,GRANULAR, "NORIT" GAC 830 : IODINE NO. MIN. 920 : MOLASSES NO. MIN. 210 : ABRASION NO. (AWWA METHOD) MIN. 75 : PARTICLE SIZE: FOR >8 MESH(2.36 MM): MAX. 15 MASS% : FOR <30 MESH(0.60MM): MAX. 4 MASS% : MOISTURE (AS PACKED): MAX. 2 MASS% : GENERAL CHARACTERISTICS: APPARENT DENSITY: 525 KG/M3 : BALL-PAN HARDNESS: 97 : UNIFORMITY COEFFICIENT: 1.6-1.7 : EFFECTIVE SIZE: 0.9-1.2 MM. : ASH CONTENT: 8-9 MASS% : REF: "NORIT GAC 830" NETHERLAND OR EQUIVALENT. |
| 22 | ACTIVATED CARBON, "NORIT" PK : IODINE NUMBER 800 : METHYLENE BLUE ADSORPTION 11 : TOTAL SURFACE AREA(B.E.T.) 875 M2/G : APPARENT DENSITY 290 KG/M3 : EFFECTIVE SIZE 1.2 MM. : UNIFORMITY COEFFICIENT 1.8 : ASH CONTENT 8 MASS % : PH : ALKALINE : MOISTURE (AS PACKED) : 2 MASS % : REF: "NORIT" TYPE PK 1-3 OR APPROVED EQUIVALENT. |
| 23 | FILTRATION AID, "REHOFIX MK 100" : COLOR: YELLOW-BROWN : PH VALUE: 5.5 : GRAIN SIZE: 80-120 MICRON : APPARENT DENSITY: 1 G/CM3 APPROX. : FLASH POINT: 185 DEG.C. APPROX. : IGNITION POINT: 205 DEG.C. APPROX. : MANUFACTURE: RET J. RETTENMAIER & SOHNE OR EQUAL. |
| 24 | FILTRATION AID , CELLULOSE (ARBOCEL) : CELLULOSE CONTENT: 99.5% APPROX. : AVERAGE FIBRE LENGTH: 300 MICRON : AVERAGE FIBRE THICK. : 20 MICRON : BULK DENSITY: 70-90 G/L : WHITENESS (VALUE AT 461 NM.): 86-/+5 % : RESIDUE ON IGNITION(850 DEG.C.): 0.3% APPROX. : PH VALUE: 6-/+1 : MANUFACTURER: J. RETTENMEIER & SHONE GMBH, GERMANY |
| 25 | NATURAL CELLULOSE FIBER ARBOCEL NV00 : NATURAL CELLULOSE FIBER ARBOCEL NV00 : BASIC RAW MATERIAL: PURE CELLULOSE : CHARACTERISTIC: SHORT FIBER, WHITE : PHYSICAL AND CHEMICAL PROPERTIES: : CELLULOSE CONTENT: APPROX. 98% : AVERAGE FIBER LENGTH: 120 MICRON : AVERAGE FIBER THICKNESS: 30 MICRON : BULK DENSITY: 250 G/L - 330 G/L : WHITENESS (ABSOLUTE VALUE AT 461 NM): MIN. 70% : PH VALUE: 7.5 -/+1.5 : SCREEN RESIDUE (IN ACCORDANCE WITH DIN 53 734/AIR JCT SIEVE) : WITH AN INTERIOR MESH APERTURE OF: 300 MICRON (MAX. 0.5%) : 100 MICRON (MAX. 30%), 32 MICRON (MIN. 50%) : MANUFACTURER: JRS (J. RETTENMAIER & SHONE) GMBH, GERMANY |
| 26 | BIOCIDE, ISOTHIAZOLINE COMPOUND : NONIONIC ISOTHIAZOLINE COMPOUND MICROBIOCIDE : IT HAS EFFECTIVENESS AGAINST BACTERIA, FUNGI AND ALGAE : SPECIFIC GRAVITY AT 25 DEG.C.: 1.07-/+0.05 : PH: 4-8, APPEARANCE: COLORLESS TO YELLOW LIQUID : MANUFACTURER: "ROSOUBGIRI" RBZOLE |
| 27 | ANTI SCALE : APPEARANCE: YELLOW TO RED BROWN CLEAR LIQUID : ODOR: SLIGHT, THERMAL STABILITY: STABLE UP TO 280 DEG.C. : SPECIFIC GRAVITY (AT 20 DEG.C.): 1.1 TO 1.2 : PH: LESS THAN 2 : MANUFACTURER: "ROSOUBGIRI" CO. RSCO-SCALEGARD EV-2050 : NOTE: IT IS USED AS SUBSTITUTE OF "BELGARD EV 2050" |
| 28 | CORROSION INHIBITOR "PL-330" : IT IS BLEND OF IMIDAZOLINE & DIETHYLAMINE IN : AROMATIC HYDROCARBON SOLVENT. : IT HAS APPLICATION IN DISTILLATION OVERHEAD : SYSTEMS SINCE IS DESIGNED TO PROTECT AGAINST : CORROSION DUE TO LOW PH & HIGH TEMPERATURE. : IT CONTROLS CORROSION DUE TO H2S, CO2 MINERAL & : ORGANIC ACIDS. : APPEARANCE: AMBER LIQUID : SPECIFIC GRAVITY AT 20 DEG.C.: 0.86-0.90 : FLASH POINT: MORE THAN 5 DEG.C. : POUR POINT: LESS THAN -5 DEG.C. : SOLUBILITY: SOLUBLE IN HYDROCARBONS : VISCOSITY AT 40 DEG.C.: 0.5-2 CST. : SUPPLIER: PARS LIAN CHEMICAL |
| 29 | CORROSION INHIBITOR, NALCO PL5550, PARS LIAN IRAN : CHEMICAL CORROSION INHIBITOR : ODOUR : ALCOHOLIC : APPEARANCE: BROWN : DENSITY AT 20 DEG.C 0.99-1.0 KG/LT : FLASH POINT : <40 DEG.C : POUR POINT:< 0 DEG.C, VISCOSITY AT 40 DEG.C.:5-15 CST. : NOTE: SIMILAR TO TYPE PL5550 NALCO(PARS LIAN IRAN) : IN APPROVED CONTAINER |
| 30 | DEMULSIFIER, PL5110 PARS LIAN : BLEND CONTAINING OXYALKYATED IN AN ISOBUTANOL AND : HYDROCARBON SOLVENT SYSTEM : PHYSICAL STATE LIQUID : COLOUR: AMBER, ODOR: AROMATIC : VISCOSITY AT 40 DEG.C.: 20-35 CST. : POUR POINT: -40 DEG.C, FLASH POINT: > 50 DEG.C. : DENSITY AT 15 DEG.C.: 0.91-0.94 G/CM3 : NOTE: SIMILAR TO TYPE PL5110 PARSLIAN OR NALCO EC-2266A : OR EQUIVALENT |
| 31 | RELEASE AGENT, SILICONE : NONIONIC OIL IN WATER EMULSION OF POLYSILOXANE : CONTAINING ALKYL AND ARALKYL GROUPS. : APPEARANCE: WHITE AQUA LIQUID : SOLID CONTENT: APPROX. 35% TO 37% WT : PH VALUE AT 25 DEG.C.: 5-7 : MANUFACTURER: "CHEMI CONTROL PARS" CCP-6440 |
| 32 | : CORROSION INHIBITOR, EN-97S : FORM: WHITE CRYSTALS OR POWDER : PH(1% IN DM WATER) : 7.3-8.2 : SOLUBILITY IN TAP WATER : SOLUBLE : SOLUBILITY IN 5% SULFAMIC ACID SOLUTION: SOLUBLE : SUPPLIER: ENERGY CHEMICAL CO. SEMNAN,TEL:22058846 |
| 33 | CORROSION INHIBITOR, NALCO 8539 : FORM: LIQUID : COLOR: RED : ODOR: SLIGHT : BOILING POINT: 100 DEG.C. (ASTM D-86) : FLASH POINT: MORE THAN 100 DEG.C. : VAPOUR PRESSURE: SAME AS WATER : RELATIVE DENSITY: 1.31 G/CM3 (ASTM D-1298) : SOLUBILITY IN WATER: COMPLETE : PH (NEAT,20 DEG.C.): 13.5 : VISCOSITY AT 20 DEG.C. : 5 CPS (ASTM D-2983) : FREEZING POINT: -8 DEG.C. (ASTM D-1177) : SUPPLIER: NALCO OR APPROVED EQUIVALENT. |
| 34 | : FLOATATION AGENT, NALCO 7132 : PHYSICAL STATE: LIQUID : APPEARANCE: AMBER : ODOR: AMMONIACAL : SPECIFIC GRAVITY: 1.14-1.18 AT 25 DEG.C. : DENSITY: 9.5-9.8 LB/GAL : SOLUBILITY IN WATER: EMULSIFIABLE : PH : 3-4 : VISCOSITY: 400-900 CPS AT 25 DEG.C. : FREEZING POINT: -12 DEG.C. : BOILING POINT: 99 DEG.C. : VAPOUR PRESSURE: 8.4 MMHG AT 0 DEG.C. : VAPOUR DENSITY: 1 : VOC CONTENT : 0% EPA METHOD 24 : REF: NALCO 7132 OR EQUIVALENT. |
| 35 | DEMULSIFIER, PL5110 PARS LIAN : BLEND CONTAINING OXYALKYATED IN AN ISOBUTANOL AND : HYDROCARBON SOLVENT SYSTEM : PHYSICAL STATE LIQUID : COLOUR: AMBER, ODOR: AROMATIC : VISCOSITY AT 40 DEG.C.: 20-35 CST. : POUR POINT: -40 DEG.C, FLASH POINT: > 50 DEG.C. : DENSITY AT 15 DEG.C.: 0.91-0.94 G/CM3 : NOTE: SIMILAR TO TYPE PL5110 PARSLIAN OR NALCO EC-2266A : OR EQUIVALENT |
| 36 | CORROSION INHIBITOR, USED IN CLOSED SYSTEM : APPEARANCE: BROWN-YELLOW LIQUID : PH: 12.5-/+0.5 : SOLUBILITY IN WATER: MISCIBLE : HAVING NITRITE SALTS : MANUFACTURER: "ROSOUBGIRI" CO. RCC100C TEHRAN |

- آدرس محل ارسال رزومه : عسلويه – مجتمع گاز پارس جنوبي – پالايشگاه دوم – اداره خريد ستاد – گروه خريد شيميايي – اتاق 224- مسئول گروه خريد اقلام شيميايي : عبدالحسين بارگاهي
تلفن : 2242 -2248 131  0773  اقدام فرماييد .

روابط عمومي شركت مجتمع گاز پارس جنوبي